## Slide 1
Intelligent Grasp Failure Detection and Autonomous Recovery
UR10 Robot · OAK-D Lite · OnRobot RG2 · CLIP Vision
Myu Wai Shin · PDE3802 Final Year Project · Middlesex University · 2025/26

## Slide 2
Introduction
Problem
• Pick-and-place is a fundamental robot task — but standard systems assume the pick always works.
• In practice, grasps fail silently: the robot carries an empty gripper to the place position.
• This work focuses on the under-studied problem of adding intelligence to detect and recover from failures.
• Key question: does the robot know it failed? What does it do about it?
This Project
• Two-part pipeline:
‒ Grasp failure detection — did the robot actually pick the object?
‒ Failure recovery — retry intelligently if it failed
• Combined into a fully autonomous end-to-end pick-and-place loop.
• System flowchart shows the complete decision path: detect target → pick → verify → recover if failed.

## Slide 3
Aims & Objectives
Aim: Develop an autonomous pick-and-place system that can detect grasp failures and recover.
• YOLO object detection — locate objects and classify them (cube / cylinder)
• Pose estimation — transform detected object position to robot coordinate frame
• Read and interpret gripper IO signals — width (AI2 voltage) and contact force (DI8)
• Train a binary visual classifier (CLIP + SVM probe) to confirm object in gripper
• Implement 3-layer grasp failure detection: width → contact → visual (CLIP)
• Develop slip detection during transit using continuous gripper monitoring
• Integrate detection + recovery into a full end-to-end autonomous pipeline
• Evaluate against quantitative targets: TPR ≥ 85%, TNR ≥ 85%, FPR < 20%, task completion ≥ 70%

## Slide 4
Hardware & Software
What the system is built on

## Slide 5
Hardware
Robot + Gripper
• Universal Robots UR10
‒ Industrial 6-DOF collaborative arm with built-in IO registers
‒ TCP/IP interface (ports 29999 and 30002) for robot control and sensor streaming
‒ Does not expose grip force directly — must be read via secondary interface
• OnRobot RG2 Parallel Jaw Gripper
‒ Width sensor via AI2 (analog voltage, calibrated 10.5–91 mm)
‒ Contact force limit via DI8 (digital signal HIGH when force limit reached)
‒ Gripper programs loaded as URP files via teach pendant
Camera & Sensor Fusion
• OAK-D Lite (Luxonis)
‒ RGB-D stereo camera — provides colour image and depth per pixel
‒ Eye-in-hand mount — wrist-mounted, moves with robot TCP
‒ Used for: object detection, pose estimation, and CLIP visual verification
• Why not just one sensor?
‒ Width alone can't distinguish a missed pick from a loose grip
‒ DI8 alone fires on partial contact
‒ Vision (CLIP) adds a redundant 3rd check — catches edge cases both sensors miss

## Slide 6
Software & Libraries
Core Libraries
• Python 3.10 — primary development language
• DepthAI SDK — OAK-D Lite camera driver and pipeline API
• OpenCV (cv2) — image processing, ArUco detection, display
• PyTorch + CUDA — GPU inference for CLIP and YOLO
• OpenAI CLIP (ViT-B/32) — visual verification classifier
• scikit-learn — SVM probe training on CLIP embeddings
• Ultralytics YOLOv8 / YOLOv5 — object detection and OBB
Communication & Tools
• socket + struct — binary packet decoding from UR secondary interface
• threading — background sensor monitoring, parallel robot/camera loops
• numpy — coordinate transforms, linear algebra
• Pillow (PIL) — image preprocessing for CLIP
• autodistill + GroundingDINO — auto-annotation of training dataset
• OpenCV calibrateHandEye() — eye-in-hand calibration solver
• URScript via port 30002 — direct robot motion commands

## Slide 7
Object Detection
YOLO + OBB on OAK-D Lite

## Slide 8
YOLO Object Detection
Training & Deployment
• YOLOv5n, YOLOv8n, YOLOv8-OBB models trained on custom dataset
• V3 dataset: 2,525 images, cubes and cylinders, auto-annotated with GroundingDINO
• Deployed on OAK-D Lite using DepthAI pipeline (on-device inference)
• Depth estimate per detection from stereo disparity map
Key Modifications
• Modifications made for reliability:
‒ Increased confidence threshold — filter out low-confidence detections
‒ NMS IoU threshold reduced — suppress overlapping duplicate boxes
‒ Temporal smoothing — only report detection if seen for 3 consecutive frames
• OBB (Oriented Bounding Box) — gives object orientation for best grip angle
‒ Standard box can't tell orientation of a cylinder or cube
‒ OBB wraps tightly and provides rotation angle
‒ Allows gripper to align to best pick orientation

## Slide 9
YOLO — Limitations & Notes
• OBB model trained on slow camera rotation sweep — good for orientation but limited viewpoints
• Mosaic augmentation during training caused confusion with backgrounds
• Low confidence on edge cases; temporal smoothing helps but adds latency
• No collision avoidance — detection does not account for robot arm obstructing view
• Works best on simple objects (cubes, cylinders); complex shapes need larger vision models
• Auto-annotation (GroundingDINO) can over-fire — ~10 false boxes/image at low threshold
• Not 100% accurate — failure detection pipeline adds a safety net on top of detection errors

## Slide 10
Pose Estimation
Eye-in-hand calibration → robot frame

## Slide 11
Pose Estimation
Calibration
• Goal: transform detected object pixel location into robot base-frame XYZ coordinates
• Camera configuration: Eye-in-hand — OAK-D Lite mounted on robot wrist (TCP)
• Calibration is critical — without it, camera and robot frames are misaligned
• Hand-eye calibration solves: camera → TCP rigid transform (R, t)
• Used OpenCV calibrateHandEye() with 5 solver methods (Tsai, Park, Horaud…)
• 20–40 pose samples collected at varied positions and wrist angles
• Reprojection error < 2.0 px (excellent), < 5.0 px (acceptable)
Detection → Robot Frame
• ArUco marker placed on pick target for reliable 6-DoF pose detection
• PyStep: detect corners → solvePnP → tag pose in camera frame
• Transform chain:
‒ Tag (camera frame) × R_cam2tcp → Tag (TCP frame)
‒ Tag (TCP frame) × FK (live robot pose) → Tag (base frame)
‒ Output: XYZ pick target in mm (robot coordinates)
• Visual alignment HUD: live TCP crosshair vs. tag centre overlay for verification
• Limitation: calibration must be re-run if camera mount shifts

## Slide 12
Failure Detection Pipeline
3-layer grasp verification + slip

## Slide 13
Reading Gripper IO Signals
Communication
• All signals read from UR secondary interface — port 30002 binary stream
• Python struct module decodes binary packets in real time
• Background daemon thread updates sensor state continuously
• AI2 (Analog Input 2): gripper width voltage
‒ Raw voltage 0–3.7 V → raw mm 0–110 mm
‒ Linear calibration applied (slope 1.405, offset -1.44)
‒ Fully open ≈ 91 mm | Fully closed ≈ 10.5 mm
Signal Interpretation
• DI8 (Digital Input 8 / TDI1): contact force flag
‒ Goes HIGH when gripper reaches force limit (object contacted)
‒ Used as a boolean: HIGH = contact confirmed, LOW = no contact
• UR10 does not expose raw grip force — DI8 is the available signal
• Gripper state logic:
‒ width ≥ 75 mm → gripper still open (close command failed)
‒ width < 11 mm → fully closed, missed object
‒ 12 < width < 75 mm AND DI8 HIGH → object confirmed

## Slide 14
Grasp Failure Detection — Architecture
Three independent detection layers — each is a hard gate:
Layer 1 · Width Sensor (AI2)
Width in target range? Did the close command run?
Layer 2 · Contact Signal (DI8)
DI8 HIGH? Force limit reached = object being gripped.
Layer 3 · CLIP Visual Check
Camera image classified as 'Holding' ≥ 75% confidence?
DESCEND → CLOSE → [Layer 1+2: width + DI8] → LIFT → [Post-lift width] → [Layer 3: CLIP] → TRANSFER
• Any layer failing triggers retry (up to MAX_RETRIES = 3)
• Each failure path logs a specific failure type to the terminal

## Slide 15
Slip Detection During Transit
Problem & Approach
• Problem: object can slip OUT of gripper after grasp is confirmed — during movement
• Standard detection only checks at pick point — misses mid-transfer drops
• Solution: activate slip monitoring loop immediately after successful CLIP verification
• Loop-close URP: gripper re-closes every cycle during transit, compensating micro-slips
• Background thread monitors AI2 width continuously while robot moves
Slip Logic
• Slip event logic:
‒ Had object (width > 11 mm after pick) = True
‒ Width drops below 11 mm during transit → slip detected
‒ _slip_detected flag set → pipeline pauses
• On slip detected: CLIP re-verify triggered automatically
‒ If CLIP still says 'Holding' → false alarm, continue
‒ If CLIP says 'Empty' → object lost, return and retry
• This adds a 4th check not possible with gripper sensors alone

## Slide 16
CLIP Visual Verification
What CLIP Is
• CLIP (Contrastive Language–Image Pre-training) — OpenAI, ViT-B/32
• Encodes images and text into the same embedding space
• Similarity between image embedding and 'a gripper holding an object' vs 'an empty gripper'
• Originally zero-shot: no labelled gripper images needed
• Upgraded: trained a lightweight SVM probe on top of CLIP embeddings
‒ Custom dataset: 600+ images of gripper holding / empty states
‒ Collected with OAK-D Lite camera at pick verification height
‒ SVM probe trained on CLIP features → 'Holding' / 'Empty'
How It Is Used
• Integration in pipeline:
‒ Robot lifts to verification height (200 mm above pick Z)
‒ Live camera frame captured — gripper region cropped
‒ CLIP encodes crop → SVM probe classifies
‒ Result displayed on monitor: label + confidence %
‒ Result auto-expires after 3 s — window resets to standby
• Two stages:
‒ 'Grasp Verification' — after initial lift
‒ 'Slip Re-verify' — after slip event detected during transit
• Threshold: ≥ 75% confidence to pass; below = fail / retry

## Slide 17
Recovery
Recovery strategy: re-approach and retry (up to MAX_RETRIES = 3)
• Layer 1 fail (width / DI8): open gripper → return to pick approach → close and recheck
• Layer 2 fail (post-lift width): open gripper → return to pick approach → retry
• Layer 3 fail (CLIP): open gripper → return to approach → retry from top
• Slip mid-transit: CLIP re-verify first → if still lost, return to pick and retry
• After MAX_RETRIES exhausted: pipeline reports failure and halts
⚠ Current Status — Work In Progress
• Detection of each failure type is fully implemented
• Re-approach and retry loop is implemented
• Advanced recovery strategies (e.g. adjusting pick pose, re-scanning) are planned but not yet integrated
• Limitation: calibration failure and collision avoidance are outside current scope

## Slide 18
End-to-End Autonomous Pick-and-Place
1. Detect
YOLO + DepthAI detect object. Depth gives approx Z.
2. Locate
ArUco marker → pose estimation → robot XYZ coords.
3. Approach
Robot moves to pick approach height (100 mm above).
4. Grip
Descend → close RG2 → settle 1.5 s.
5. Check 1
Width + DI8: object in gripper? If fail → retry.
6. Lift
Raise to CLIP verification height (200 mm above pick Z).
7. Check 2
Post-lift width: still holding? If not → slip during lift.
8. CLIP
Visual verification: 'Holding' ≥ 75%? If fail → retry.
9. Transit
Transfer to place position with slip monitor active.
10. Place
Lower → open gripper → retract → task complete.
✓ All stages run autonomously in a loop — no human intervention required between picks.

## Slide 19
Testing & Results
Evaluation protocol and outcomes

## Slide 20
Testing & Evaluation Targets
90-trial evaluation protocol — 30 successful grasps, 30 failed grasps, 30 slip events
Metric
Formula
Target
Meaning
True Positive Rate (TPR)
TP / (TP + FN)
≥ 85%
Successful grasps correctly confirmed
True Negative Rate (TNR)
TN / (TN + FP)
≥ 85%
Failed grasps correctly identified
False Positive Rate (FPR)
FP / (FP + TN)
< 20%
System says success when grasp failed
Overall Accuracy
(TP + TN) / 90
≥ 85%
Combined correct verdicts across all trials
Recovery Success Rate
Recoveries succeeded / attempted
≥ 70%
Failed grasps resolved by recovery
End-to-end Completion
Successful placements / 90
≥ 70%
Overall system performance

## Slide 21
Results
[INSERT RESULTS TABLE / CHARTS HERE]
• Report measured TPR, TNR, FPR, Overall Accuracy, Recovery Rate, Task Completion Rate
• Show comparison: detection-only pipeline vs. full detection + recovery pipeline
• Include demo video screenshots or frames showing: successful pick, detected failure, recovery
• Highlight any cases where CLIP disagreed with width/DI8 — discuss sensor fusion benefit
→ Add your actual measured values and video evidence here before presenting.

## Slide 22
Limitations & Future Work
Current Limitations
• No collision avoidance — robot does not model obstacles in workspace
• Calibration drift — hand-eye calibration must be re-run if camera shifts
• CLIP accuracy not 100% — uncertain predictions on poor lighting or extreme crops
• Gripper force not readable from Python — only binary DI8 contact flag available
• Recovery re-approach assumes object is still in the same position
• No object re-detection if object moves between attempts
Future Work
• Advanced recovery strategies (adjust pick pose, rotate approach angle)
• Replace URP-based gripper control with direct force torque sensing
• Extend CLIP training dataset for more challenging lighting/backgrounds
• Add object re-detection before each retry attempt
• Generalise to arbitrary objects (beyond cubes and cylinders)
• Integrate with motion planning for collision-aware trajectories

## Slide 23
Summary
• Built a 3-layer grasp failure detection pipeline: width + DI8 + CLIP visual
• Implemented slip detection via continuous gripper monitoring during transit
• Integrated CLIP (ViT-B/32) + custom SVM probe for vision-based grasp confirmation
• Developed end-to-end autonomous pick-and-place with detection and recovery loop
• Evaluation targets: TPR ≥ 85%, FPR < 20%, Task completion ≥ 70%
Myu Wai Shin · PDE3802 Final Year Project · Middlesex University · 2025/26