## Slide 1
Intelligent Grasp Failure Detection and Autonomous Recovery
UR10 · OnRobot RG2 · OAK-D Lite · CLIP Vision
Myu Wai Shin · PDE3802 Final Year Project · Middlesex University · 2025/26

## Slide 2
Introduction
The Problem
Robotic pick-and-place systems assume the grasp works. When it fails, the robot carries an empty gripper — unaware. This is a critical gap: the system does not know it failed.
This Project
① Detect whether the grasp succeeded
② If it failed — detect why and recover
③ Loop: fully autonomous pick-and-place
Focus: adding intelligence to what happens after a failure — not just training the robot to pick.

## Slide 3
Aims & Objectives
Aim: Develop an autonomous pick-and-place system capable of detecting grasp failures and recovering.
1
YOLO Object Detection
Locate and classify objects (cube / cylinder) in the workspace
2
Pose Estimation
Transform pixel detection → robot XYZ coordinates
3
Gripper IO Signals
Read width (AI2) and contact force (DI8) from RG2 in real time
4
Visual Classifier (CLIP)
Linear probe on CLIP embeddings: confirm object in gripper
5
3-Layer Failure Detection
Width → Contact → CLIP: redundant independent checks
6
Slip Detection
Monitor grip during transit; detect mid-move object loss
7
Recovery Integration
Retry loop: return to pick, re-approach, re-verify

## Slide 4
Hardware & Software
What the system is built on

## Slide 5
Hardware
UR10 Robot Arm
• 6-DOF industrial collaborative arm
• TCP/IP interface (ports 29999 & 30002)
• IO registers: AI2 (analog) + DI8 (digital)
OnRobot RG2 Gripper
• Parallel jaw — max 110 mm width
• AI2: width voltage (calibrated ±1 mm)
• DI8: HIGH when force limit reached
OAK-D Lite Camera
• RGB-D stereo — colour + depth per pixel
• Eye-in-hand: wrist-mounted, moves with TCP
• Detection · Pose · CLIP verification
Why width + force + vision? — Each sensor catches failures the others miss. Width alone can't confirm contact; DI8 fires on partial touch; CLIP adds a visual ground truth.

## Slide 6
Software & Libraries
Robot Control
• socket + struct — binary UR packet decoding
• URScript via port 30002 — motion commands
• URP files (teach pendant) — gripper control
Vision & Detection
• DepthAI SDK — OAK-D Lite pipeline
• OpenCV — ArUco, image processing, display
• Ultralytics YOLOv8 / YOLOv5 OBB
AI & Classification
• PyTorch + CUDA — GPU inference
• OpenAI CLIP ViT-B/32 — image embeddings
• scikit-learn — Logistic Regression (linear probe)
Data & Tools
• numpy + Pillow — transforms, preprocessing
• GroundingDINO + autodistill — auto-annotation
• OpenCV calibrateHandEye() — eye-in-hand solver

## Slide 7
Object Detection
YOLO + OBB on OAK-D Lite

## Slide 8
YOLO Object Detection
Training & Deployment
Models: YOLOv5n, YOLOv8n, YOLOv8-OBB
Dataset V3: 2,525 images — cubes & cylinders
Auto-annotated with GroundingDINO
Deployed on OAK-D Lite via DepthAI pipeline
Depth estimate from stereo disparity per detection
Key Modifications
Confidence Threshold ↑
Raised threshold to filter out weak detections
NMS IoU ↓
Suppresses duplicate overlapping boxes
Temporal Smoothing
Only reports object if seen for 3 consecutive frames
OBB — Orientation
Oriented Bounding Box gives rotation angle → best grip

## Slide 9
Pose Estimation
Eye-in-hand calibration → robot frame

## Slide 10
Pose Estimation
Camera Calibration
Intrinsics via charuco board
→
Hand-Eye Calibration
20–40 poses → OpenCV calibrateHandEye() solves camera→TCP
→
ArUco Detection
6×6 marker on target → 6-DoF pose in camera frame
→
Coord Transform
Camera → TCP → Base frame using FK (live robot pose)
→
Robot XYZ Output
Pick target in mm in robot base frame
Eye-in-hand: camera moves with the wrist — calibration gives a fixed camera→TCP offset, valid for all robot poses. Reprojection error achieved: < 2.0 px.
Limitations
• Calibration must be re-run if camera mount shifts
• Assumes ArUco marker is placed on or near the pick target
• Accuracy depends on board detection quality and number of poses collected

## Slide 11
Failure Detection Pipeline
Gripper signals · Visual verification · Slip detection

## Slide 12
Reading Gripper IO Signals
AI2 — Width (Analog)
Gripper finger spread in mm
• Voltage read from UR secondary interface (port 30002)
• Raw voltage → raw mm → calibrated mm
• Linear calibration: slope 1.405 · offset -1.44
• Fully open ≈ 91 mm | Fully closed ≈ 10.5 mm
• Accuracy: ± 1 mm
DI8 — Contact Force (Digital)
ON/OFF flag when force limit reached
• Digital register read from same binary stream
• HIGH = gripper reached programmed force limit
• Acts as a contact confirmation signal
• UR10 does not expose raw force value — DI8 is the available signal
• Background daemon thread monitors both signals at ~25 Hz
width ≥ 75 mm
Gripper still open — close command failed
width < 11 mm
Fully closed — missed object
12–75 mm & DI8 HIGH
Object confirmed ✓

## Slide 13
Grasp Failure Detection — 3 Layers
Layer 1 · Width + DI8
Checks:
Width in valid range? & DI8 HIGH (contact)?
Checks immediately after gripping
FAIL → retry
PASS → next
Layer 2 · Post-lift Width
Checks:
Width still > 11 mm after lifting?
Catches objects slipped during lift
FAIL → retry
PASS → next
Layer 3 · CLIP Visual
Checks:
Camera: 'Holding' ≥ 75% confidence?
Visual ground truth — independent of sensors
FAIL → retry
PASS → next
DESCEND → GRIP → [L1] → LIFT → [L2] → [L3: CLIP] → TRANSFER → [Slip?] → PLACE

## Slide 14
CLIP Visual Verification
What is CLIP?
CLIP (OpenAI, ViT-B/32) encodes images and text into the same vector space — making it possible to compare an image directly to a text description. Image crop of gripper → CLIP → 512-dim feature vector A Logistic Regression linear probe is trained on top of these features using ~600 real gripper images: • Holding (object between fingers) • Empty (no object) Result: label + confidence % in < 200 ms.
In the Pipeline
① Lift to CLIP height
200 mm above pick position
② Flush camera buffer
0.6 s settle — ensures fresh, sharp frame
③ Crop gripper region
Fixed crop centred on gripper tip
④ CLIP → Linear probe
'Holding' or 'Empty' + confidence
⑤ ≥ 75% 'Holding'
✓ Pass — continue to transfer
⑤ < 75% or 'Empty'
✗ Fail — open, return, retry

## Slide 15
Slip Detection During Transfer
Problem: gripper sensors only checked at pick point — object can still slip during transit with no detection.
How It Works
Loop-close URP: gripper re-closes continuously during transit
Background thread reads AI2 width at ~25 Hz
If width drops below 11 mm mid-transit → slip flag set
CLIP re-verify triggered immediately
Slip Response
CLIP re-verify
Triggers after slip flag set
Still 'Holding'
False alarm → continue to place
'Empty'
Object lost → return to pick, retry

## Slide 16
Recovery
Strategy: re-approach and retry — up to MAX_RETRIES = 3
Layer 1 fail (width / DI8)
Open gripper → return to pick approach → re-close → recheck
Layer 2 fail (post-lift width)
Object slipped on lift → open → descend → retry full grip
Layer 3 fail (CLIP)
Visual not confirmed → open → return to approach → retry from top
Slip during transit
CLIP re-verify → if lost, return to pick and retry
⚠ Detection and retry loop: implemented. Advanced recovery (adapt pick pose, re-scan): Work in Progress.
✓ Currently working: failure type identified, gripper opened, robot returns to pick approach, retries up to 3×.

## Slide 17
End-to-End Autonomous Pipeline
1 Detect
YOLO + depth
→
2 Locate
ArUco → robot XYZ
→
3 Approach
100 mm above pick
→
4 Grip
Descend + close RG2
→
5 Check L1
Width + DI8
6 Lift
+200 mm
→
7 Check L2
Post-lift width
→
8 CLIP
≥75% Holding
→
9 Transfer
Slip monitor ON
→
10 Place
Lower + release
✓ Fully autonomous loop — no operator input between picks.

## Slide 18
Testing & Results
90-trial evaluation protocol

## Slide 19
Evaluation — 90-Trial Protocol
30 successful picks · 30 failed picks · 30 slip events
Metric
Formula
Target
Interpretation
True Positive Rate
TP / (TP + FN)
≥ 85%
Success correctly confirmed
True Negative Rate
TN / (TN + FP)
≥ 85%
Failure correctly detected
False Positive Rate
FP / (FP + TN)
< 20%
Says success when actually failed
Overall Accuracy
(TP + TN) / 90
≥ 85%
All correct decisions
Recovery Success Rate
Recovered / Attempted
≥ 70%
Failures resolved by recovery
Task Completion Rate
Placements / 90
≥ 70%
End-to-end performance

## Slide 20
Results
[ INSERT RESULTS TABLE AND CHARTS HERE ]
Report: TPR, TNR, FPR, Overall Accuracy, Recovery Rate, Task Completion Rate
Show: detection-only pipeline vs. detection + recovery pipeline comparison
Include: screenshots from demo video — successful pick, detected failure, recovery sequence

## Slide 21
Limitations & Future Work
Current Limitations
• No collision avoidance — robot does not detect obstacles in workspace
• Calibration drift — hand-eye re-calibration needed if camera shifts
• CLIP accuracy not 100% — poor lighting / unusual crop angles cause errors
• No raw force readout — only binary DI8 contact flag available from UR10
• Recovery assumes object stays in the same position between retries
Future Work
• Adapt pick pose on retry — not just re-approach same point
• Re-detect object position before each retry attempt
• Replace URP gripper control with direct force-torque sensor
• Generalise beyond cubes & cylinders to arbitrary objects
• Add collision-aware motion planning

## Slide 22
What Was Built
✓ 3-layer grasp failure detection: width · DI8 contact · CLIP visual
✓ Slip detection with automatic CLIP re-verify during transit
✓ CLIP ViT-B/32 + Logistic Regression linear probe (trained on real gripper images)
✓ Fully autonomous end-to-end loop with retry recovery
✓ Evaluation targets: TPR ≥ 85% · FPR < 20% · Task completion ≥ 70%
Myu Wai Shin · PDE3802 Final Year Project · Middlesex University · 2025/26